## Slide 1
OpenEMPIRE — North Sea Extension
From the original capacity-expansion model to a performance-tuned North Sea build with offshore nodes
Ehsan Nokandi
Summary of upstream EMPIRE and the North Sea modifications in this fork

## Slide 2
ORIGINAL MODEL
What is EMPIRE?
• A stochastic capacity-expansion model for the European power system, formulated in Pyomo (open-source, MIT-licensed).
• Co-optimizes long-run investment and short-run operation under uncertainty to minimize total discounted system cost.
• Two-stage stochastic program: investment decisions per strategic period, operational decisions across sampled scenarios.
• Multi-horizon: strategic investment periods (e.g. every 5 years to 2060) each containing representative operational seasons + peak hours.
• Solved with a third-party LP solver (Gurobi / Xpress / CPLEX); a full run needs an HPC (~140 GB RAM).

## Slide 3
ORIGINAL MODEL
How the model is structured
run.py
Single entry point the user runs; selects a dataset and config.
empire.py
Abstract Pyomo formulation: sets, variables, constraints, objective, and result printing.
reader.py
Builds .tab input files from the Excel workbooks in 'Data handler'.
scenario_random.py
Samples representative time series into stochastic operational scenarios.
config.py
Configuration objects driven by config/run.yaml.
model_runner.py
Wires config, data managers and the solve together.
Inputs: 7 Excel workbooks per dataset (general, generation, node, sets, transmission, storage) → .tab files → Pyomo model. Outputs: CSV results + optional IAMC-format export.

## Slide 4
WHY CHANGE IT
Motivation for the fork
• Goal: model the North Sea region in detail — countries NO, DK, UK, NL and DE, with explicit offshore (wind) nodes and the offshore grid linking them.
• Base EMPIRE had no proper handling of offshore nodes — it crashed on datasets where offshore nodes were absent or empty.
• IAMC result export produced incorrect / incomplete output for the North Sea nodes and technologies.
• Large North Sea runs solved very slowly in Gurobi, motivating dedicated solver performance work.
• Need: handle offshore nodes robustly, diagnose infeasibilities, and accelerate the solve without changing the physics.

## Slide 5
WHAT I DID
Overview of my changes
18 commits ahead of upstream — ~370 lines of core model code; the rest is North Sea data, analysis notebooks and tooling.
1 North Sea case
NO/DK/UK/NL/DE with offshore nodes; safe loading when a dataset has no offshore nodes.
2 IAMC reporting
Correct region & generator mappings; optional offshore→onshore aggregation.
3 Solver performance
Configurable Gurobi options, emission-cap reformulation, ramping toggle.
4 Robustness
Infeasibility detection + IIS export; fixed CO2-price output bug.
5 Tooling & env
Result-analysis scripts/notebooks; pinned Python 3.11 env.

## Slide 6
CHANGE DETAIL
1 — North Sea region & offshore nodes
• Added a North Sea case covering NO, DK, UK, NL and DE, with explicit offshore (wind) nodes representing the offshore grid.
• Added a north_sea mode and offshore-node handling in empire.py (new OffshoreNode set).
  – Sets_OffshoreNode.tab is now loaded only if it exists and is non-empty — fixes a crash on datasets with no offshore nodes.
• New North Sea input dataset under Data handler/north_sea.
• Reader / tab-file generation updated to emit offshore sets correctly.
Files: empire/core/empire.py, empire/core/reader.py, Data handler/north_sea

## Slide 7
CHANGE DETAIL
2 — IAMC output corrections
• IAMC = standard reporting format for integrated-assessment / energy scenarios; EMPIRE can export results in it.
• Fixed region mapping for the new North Sea nodes, with a fallback for unknown nodes instead of failing.
• Fixed generator-name mapping: added spaced-name variants ("Wind offshore floating/grounded" → Wind|Offshore) and missing LigniteCCS / BioCCS.
• Collapsed technology-specific emission rows into the aggregate electricity-CO2 row.
• New optional flag aggregate_offshore_nodes_in_IAMC: maps each offshore node to its nearest onshore region (by coordinates) in the IAMC export.
Files: empire/core/empire.py (IAMC block), config/run.yaml, config.py

## Slide 8
CHANGE DETAIL
3 — Solver performance acceleration
• Configurable Gurobi options plumbed config.py → model_runner.py → empire.py: Method, Crossover, Presolve, Threads, ScaleFlag, NumericFocus, BarHomogeneous.
  – Defaults enable the accelerators (barrier, crossover off, aggressive presolve); robustness 'brakes' are off by default and documented as enable-on-failure only.
• Emission-cap reformulation: replaced one dense all-generators constraint row (which injected 5e-08 coefficients via /1e6) with per-node nodeEmission variables in tonnes — kills barrier fill-in and the bad matrix range.
  – Dual / CO2-price reporting updated to match the new formulation.
• use_ramping toggle: optionally drop thermal inter-hour ramp constraints to reduce temporal coupling.

## Slide 9
CHANGE DETAIL · CODE
3a — Configurable Gurobi solver options
Solver tuning was hard-coded. It is now exposed end-to-end so each run can be tuned from config/run.yaml without touching the model:
config/run.yaml
→
config.py
→
model_runner.py
→
empire.py → Gurobi
Before — hard-coded
opt.options["Crossover"] = 0
opt.options["Method"] = 2
After — configurable (config-driven)
opt.options["Method"] = solver_method
if solver_crossover is not None:
opt.options["Crossover"] = solver_crossover
if solver_presolve is not None:
opt.options["Presolve"] = solver_presolve
if solver_threads is not None:
opt.options["Threads"] = solver_threads
if solver_scaleflag is not None:
opt.options["ScaleFlag"] = solver_scaleflag
if solver_numericfocus is not None:
opt.options["NumericFocus"]= solver_numericfocus
if solver_barhomogeneous is not None:
opt.options["BarHomogeneous"]= solver_barhomogeneous
• Accelerators (defaults): Method=2 (barrier), Crossover=0 (skip the tail), Presolve=2 (aggressive).
• Brakes (off by default): ScaleFlag, NumericFocus, BarHomogeneous — robustness options that slow Gurobi; enable only on numerical failure.

## Slide 10
CHANGE DETAIL · MATH
3b — Emission cap constraint (original)
One constraint per investment period i and scenario w, summing over every generator and every operational hour:
(1 / 106) · Σ(n,g)∈GoN Σ(s,h)∈HoS ρs · φg · (3.6 / ηg,i) · pn,g,h,i,w ≤ Ci
∀ i ∈ I (periods), w ∈ W (scenarios)
• p (genOperational) = production; ρ = season scaling; φ = CO₂ factor; η = efficiency; C = CO₂ cap (Mt).
• Problem 1 — dense row: one row touches every (generator × hour) variable → hundreds of thousands of nonzeros in a single row.
• Problem 2 — bad scaling: the 1/10⁶ (Mt) factor puts ~5e-08 coefficients in the matrix, widening the range to [5e-08, 1e+01].
• Dense rows wreck the barrier Cholesky factorization (fill-in); wide ranges trigger Gurobi numerical-conditioning warnings.

## Slide 11
CHANGE DETAIL · MATH + CODE
3c — Emission cap reformulation
Introduce a per-node emission variable E (tonnes); split the dense row into sparse per-node rows + a small cap row, and move 10⁶ to the right-hand side:
Definition (sparse, per node):
En,i,w = Σg:(n,g)∈GoN Σ(s,h)∈HoS ρs · φg · (3.6 / ηg,i) · pn,g,h,i,w ∀ n ∈ N, i ∈ I, w ∈ W
Cap (sparse, |N| terms):
Σn∈N En,i,w ≤ 106 · Ci ∀ i ∈ I, w ∈ W
empire.py
model.nodeEmission = Var(model.Node, model.PeriodActive, model.Scenario, domain=Reals)
def emission_cap_rule(model, i, w):
return sum(model.nodeEmission[n,i,w] for n in model.Node) - 1e6*model.CO2cap[i] <= 0
• Each E-definition row is sparse (only that node's generators); the cap row has just |N| entries — no dense row, no barrier fill-in.
• Moving 10⁶ to the RHS removes the 5e-08 coefficients → matrix range back to [1e-03, 1e+01]. Domain = Reals (CCS gives negative CO₂; cap can go negative).
• Dual / CO₂-price reporting updated to match (the *1e6 divisor removed).

## Slide 12
CHANGE DETAIL
3 — What the performance analysis found
Diagnosis
• Barrier solve is fast; the crossover tail dominated — 9–10× the barrier time (millions of pivots).
• Wide matrix range [5e-08, …] came from the /1e6 in the emission cap, not from the input data (the tiny-value hypothesis was ruled out).
• One dense emission-cap row per (period, scenario) → catastrophic fill-in in the barrier Cholesky factor.
• Stacking NumericFocus / BarHomogeneous added 'brakes' that slowed large runs.
Fixes applied
• Crossover = 0 → removes the 9–10× tail (interior solution).
• Method = 2 (barrier) + aggressive presolve.
• Emission cap expressed in tonnes → removes 5e-08 and the dense row.
• Brakes reverted to defaults; documented to enable only on numerical failure.
• All reasoning captured in PERF_HANDOFF.md (incl. a stale editable-install gotcha on the cluster).

## Slide 13
CHANGE DETAIL
4 — Robustness & diagnostics
• Infeasibility handling: on an 'infeasible' termination the model now writes an .lp file and computes an IIS (Irreducible Infeasible Subsystem).
  – Uses the gurobipy API with a gurobi_cl subprocess fallback — so a failed run produces a diagnosable file instead of just crashing.
• Feasibility check added to prevent the model from crashing mid-build.
• Bug fix: results_co2_price_resolved.csv was never written (missing final row write) — now populated and includes a CO2Cap_Ton column.
• Node-name fixes for the North Sea dataset.

## Slide 14
CHANGE DETAIL
5 — Tooling & environment
• New result-analysis tooling: scripts/plot.py, scripts/review_results.py, and notebooks results_reviewer.ipynb & scenarios_comparison.ipynb.
• IAMC-fixing helpers (check_iamc_mappings.py, _fix_iamc_excel.py, fix_node_names.py) and a regions geojson for mapping.
• environment.yml: pinned python=3.11 and dropped the 'defaults' conda channel for reproducible setup.
• config/run.yaml: new options surfaced (north_sea, aggregate_offshore_nodes_in_IAMC, use_ramping, solver_* block) with inline guidance.

## Slide 15
Summary & impact
✓ Extended EMPIRE to a North Sea model with explicit offshore nodes.
✓ Made the model robust: no crash without offshore nodes; infeasibilities are now diagnosable via IIS.
✓ Corrected IAMC reporting for the new regions and technologies.
✓ Accelerated the solve by attacking the real bottlenecks — crossover and a dense, badly-scaled emission-cap row — not just flag-tweaking.
✓ Added analysis tooling and a reproducible environment for ongoing scenario work.
Physics unchanged where it matters — changes target resolution, reporting correctness, robustness and solver performance.